## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 8
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 8 :: Topics
Introduction
Memory System Performance Analysis
Caches
Virtual Memory
Memory-Mapped I/O
Summary

## Slide 3
Computer performance depends on:
  Processor performance
  Memory system performance
Memory Interface
Introduction

## Slide 4
In prior chapters, assumed access memory in 1 clock cycle – but hasn’t been true since the 1980’s
Processor-Memory Gap

## Slide 5
Make memory system appear as fast as processor
Use hierarchy of memories
Ideal memory:
  Fast
  Cheap (inexpensive)
  Large (capacity)
But can only choose two!
Memory System Challenge

## Slide 6
Memory Hierarchy

## Slide 7
Gives the illusion of bigger memory
Main memory (DRAM) acts as cache for hard disk
Virtual Memory

## Slide 8
Physical Memory: DRAM (Main Memory)
Virtual Memory: Hard drive
  Slow, Large, Cheap
Memory Hierarchy

## Slide 9
Takes milliseconds to seek correct location on disk
Hard Disk

## Slide 10
Virtual addresses
  Programs use virtual addresses
  Entire virtual address space stored on a hard drive
  Subset of virtual address data in DRAM
  CPU translates virtual addresses into physical addresses (DRAM addresses)
  Data not in DRAM fetched from hard drive
Memory Protection
  Each program has own virtual to physical mapping
  Two programs can use same virtual address for different data
  Programs don’t need to be aware others are running
  One program (or virus) can’t corrupt memory used by another
Virtual Memory

## Slide 11
Cache | Virtual Memory
Block | Page
Block Size | Page Size
Block Offset | Page Offset
Miss | Page Fault
Tag | Virtual Page Number
Physical memory acts as cache for virtual memory
Cache/Virtual Memory Analogues

## Slide 12
Page size: amount of memory transferred from hard disk to DRAM at once
Address translation: determining physical address from virtual address
Page table: lookup table used to translate virtual addresses to physical addresses
Virtual Memory Definitions

## Slide 13
Most accesses hit in physical memory
But programs have the large capacity of virtual memory
Virtual & Physical Addresses

## Slide 14
Address Translation

## Slide 15
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes
Virtual Memory Example

## Slide 16
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes
Organization:
  Virtual address: 31 bits
  Physical address: 27 bits
  Page offset: 12 bits
  # Virtual pages = 231/212 = 219 (VPN = 19 bits)
  # Physical pages = 227/212 = 215 (PPN = 15 bits)
Virtual Memory Example

## Slide 17
19-bit virtual page numbers
15-bit physical page numbers
Virtual Memory Example

## Slide 18
Virtual Memory Example
What is the physical address of virtual address 0x247C?

## Slide 19
Virtual Memory Example
What is the physical address of virtual address 0x247C?
  VPN = 0x2
  VPN 0x2 maps to PPN 0x7FFF
  12-bit page offset: 0x47C
  Physical address = 0x7FFF47C

## Slide 20
Page table
  Entry for each virtual page
  Entry fields:
    Valid bit: 1 if page in physical memory
    Physical page number: where the page is located
How to perform translation?

## Slide 21
VPN is index into page table
Page Table Example

## Slide 22
What is the physical address of virtual address 0x5F20?
Page Table Example 1

## Slide 23
What is the physical address of virtual address 0x5F20?
  VPN = 5
  Entry 5 in page table VPN 5 => physical page 1
  Physical address: 0x1F20
Page Table Example 1

## Slide 24
What is the physical address of virtual address 0x73E0?
Page Table Example 2

## Slide 25
What is the physical address of virtual address 0x73E0?
  VPN = 7
  Entry 7 is invalid
  Virtual page must be paged into physical memory from disk
Page Table Example 2

## Slide 26
Page table is large
  usually located in physical memory
Load/store requires 2 main memory accesses:
  one for translation (page table read)
  one to access data (after translation)
Cuts memory performance in half
  Unless we get clever…
Page Table Challenges

## Slide 27
Small cache of most recent translations
Reduces # of memory accesses for most loads/stores from 2 to 1
Translation Lookaside Buffer (TLB)

## Slide 28
Page table accesses: high temporal locality
  Large page size, so consecutive loads/stores likely to access same page
TLB
  Small: accessed in < 1 cycle
  Typically 16 - 512 entries
  Fully associative
  > 99 % hit rates typical
  Reduces # of memory accesses for most loads/stores from 2 to 1
TLB

## Slide 29
Example 2-Entry TLB

## Slide 30
Multiple processes (programs) run at once
Each process has its own page table
Each process can use entire virtual address space
A process can only access physical pages mapped in its own page table
Memory Protection

## Slide 31
Virtual memory increases capacity
A subset of virtual pages in physical memory
Page table maps virtual pages to physical pages – address translation
A TLB speeds up address translation
Different page tables for different programs provides memory protection
Virtual Memory Summary

## Slide 32
Processor accesses I/O devices just like memory (like keyboards, monitors, printers)
Each I/O device assigned one or more address
When that address is detected, data read/written to I/O device instead of memory
A portion of the address space dedicated to I/O devices
Memory-Mapped I/O

## Slide 33
Address Decoder:
  Looks at address to determine which device/memory communicates with the processor
I/O Registers:
  Hold values written to the I/O devices
ReadData Multiplexer:
  Selects between memory and I/O devices as source of data sent to the processor
Memory-Mapped I/O Hardware

## Slide 34
The Memory Interface

## Slide 35
Memory-Mapped I/O Hardware

## Slide 36
Suppose I/O Device 1 is assigned the address 0xFFFFFFF4
  Write the value 42 to I/O Device 1
  Read value from I/O Device 1 and place in $t3
Memory-Mapped I/O Code

## Slide 37
Write the value 42 to I/O Device 1 (0xFFFFFFF4)
  addi $t0, $0, 42
  sw $t0, 0xFFF4($0)
Memory-Mapped I/O Code

## Slide 38
Read the value from I/O Device 1 and place in $t3
  lw $t3, 0xFFF4($0)
Memory-Mapped I/O Code

## Slide 39
Embedded I/O Systems
  Toasters, LEDs, etc.
PC I/O Systems
Input/Output (I/O) Systems

## Slide 40
Example microcontroller: PIC32
  microcontroller
  32-bit MIPS processor
  low-level peripherals include:
    serial ports
    timers
    A/D converters
Embedded I/O Systems

## Slide 41
// C Code
#include <p3xxxx.h>
int main(void) {
int switches;
TRISD = 0xFF00; // RD[7:0] outputs
// RD[11:8] inputs
while (1) {
// read & mask switches, RD[11:8]
switches = (PORTD >> 8) & 0xF;
PORTD = switches; // display on LEDs
}
}
Digital I/O

## Slide 42
Example serial protocols
  SPI: Serial Peripheral Interface
  UART: Universal Asynchronous Receiver/Transmitter
  Also: I2C, USB, Ethernet, etc.
Serial I/O

## Slide 43
SPI: Serial Peripheral Interface
Master initiates communication to slave by sending pulses on SCK
Master sends SDO (Serial Data Out) to slave, msb first
Slave may send data (SDI) to master, msb first

## Slide 44
UART: Universal Asynchronous Rx/Tx
Configuration:
  start bit (0), 7-8 data bits, parity bit (optional), 1+ stop bits (1)
  data rate: 300, 1200, 2400, 9600, …115200 baud
Line idles HIGH (1)
Common configuration:
  8 data bits, no parity, 1 stop bit, 9600 baud

## Slide 45
// Create specified ms/us of delay using built-in timer
#include <P32xxxx.h>
void delaymicros(int micros) {
if (micros > 1000) { // avoid timer overflow
delaymicros(1000);
delaymicros(micros-1000);
}
else if (micros > 6){
TMR1 = 0; // reset timer to 0
T1CONbits.ON = 1; // turn timer on
PR1 = (micros-6)*20; // 20 clocks per microsecond
// Function has overhead of ~6 us
IFS0bits.T1IF = 0; // clear overflow flag
while (!IFS0bits.T1IF); // wait until overflow flag set
}
}
void delaymillis(int millis) { while (millis--) delaymicros(1000); // repeatedly delay 1 ms
} // until done
Timers

## Slide 46
  Needed to interface with outside world
Analog input: Analog-to-digital (A/D) conversion
  Often included in microcontroller
  N-bit: converts analog input from Vref--Vref+ to 0-2N-1
Analog output:
  Digital-to-analog (D/A) conversion
    Typically need external chip (e.g., AD558 or LTC1257)
    N-bit: converts digital signal from 0-2N-1 to Vref--Vref+
  Pulse-width modulation
Analog I/O

## Slide 47
Pulse-Width Modulation (PWM)
Average value proportional to duty cycle
Add high-pass filter on output to deliver average value

## Slide 48
Other Microcontroller Peripherals
Examples
  Character LCD
  VGA monitor
  Bluetooth wireless
  Motors

## Slide 49
Personal Computer (PC) I/O Systems
USB: Universal Serial Bus
  USB 1.0 released in 1996
  standardized cables/software for peripherals
PCI/PCIe: Peripheral Component Interconnect/PCI Express
  developed by Intel, widespread around 1994
  32-bit parallel bus
  used for expansion cards (i.e., sound cards, video cards, etc.)
DDR: double-data rate memory

## Slide 50
Personal Computer (PC) I/O Systems
TCP/IP: Transmission Control Protocol and Internet Protocol
  physical connection: Ethernet cable or Wi-Fi
SATA: hard drive interface
Input/Output (sensors, actuators, microcontrollers, etc.)
  Data Acquisition Systems (DAQs)
  USB Links